INTRO:

The subject of this thesis is about generating and verifying hardware with more than one level.

SLIDE 1, INTRODUCTION:

-1 >>
      The idea is to generate ARMs advanced high performance bus architecture at the electronic
      system level and register transfer level for a user defined number of masters and slaves.

      It is also to generate properties from the ESL model, and automatically refine them
      such that they hold on the corresponding RTL design.

-2 >>
      There are two main goals:
      One, is that a high level of abstraction is achieved in the ESL model.

      Two, is that the ESL is a sound abstraction of the RTL.

SLIDE 2, GENERATOR:

-1 >>
       The generator is a C++ program, it takes number of masters and slaves as input arguments.
       It reads a text file containing the slave address ranges, this file is configurable by the user.
       It uses this data to generate models at the ESL and RTL.

       The generator calls a DeSCAM plugin with the ESL modules.
       Abstract models are created, and recognizable names in these models are used to create
       and refine signal and state macros.

       The property sets are printed, the duration of certain properties are modified in the process.
       Completeness descriptions are subsequently created.

SLIDE 3, ESL OVERVIEW:

-1 >>
      Here is an overview of the model at the electronic system level.
      It is not feasible to describe the entire system within a single module.
      Each master agent can receive a payload and issue a request at any given time.
      Because of this parallelism, there are simply too many possibilities to account for.

      The figure show a system with two master agents.
      The connection between the agents and the bus model the AHB master interface from the
      protocol.

      The majority of this interface is modeled using these shared ports directly between the
      agents and bus.
      There are three signals of the interface which control the transfer flow, they need to be modeled
      using an emulated port.
      These are the signals request, and in turn grant, as well as ready.
      This module does not act as a separate SystemC-PPA. It is for the purpose of this work,
      considered a port interface.

SLIDE 4, ESL CONTINUED:

-1 >>
      Here are the FSMs! the master agent on the left, and the bus matrix on the right.
      Both have a set of important states which must be reflected in the ESL model.
      The bus matrix controls when the agent advances through the majority of its state machine.

      Here a request is issued, and the states advance on both sides.

-2 >>
      The case with the AHB is tricky, because multiple masters act in parallel, and the transfer phases
      are pipelined.
      Here a request is issued from a second master as the first one is being processed.
      The second request is granted, as the first request advances to the data phase.

-3 >>
      After the slaves have processed the first request, a third request may be granted.
      Simultaneously, the second request is advanced to the data phase as the first one is ended.
      This behavior is handled through the blocking interface, to maintain a good level
      of abstraction.

SLIDE 5 BUS MATRIX, SLAVE INTERFACE:

-1 >>
      Here is a quick overview of the data state in the bus matrix.
      We fetch the data part of the payload at this stage, to reflect that data is sampled
      in the data phase.
      The payload is forwarded to the slave, and response is immediately awaited.

      The response contains transfer status: success or error, as well as data if it was a read.
      Response payload is written to all masters.

      Transfers outside the slave range provide a default error response.

      The request handling over the blocking ports must occur here at the end, and here only.
      This is why we use shared ports for the remaining parts of the interface.
      we want the data to reach its target, without breaking protocol.

SLIDE 6, EMULATED PORT, REASON:

-1 >>
      The parallel and pipelined requests and transfer phases using the blocking ports requires a
      workaround.
      Consider the case of the data state;
      We might have one request and two active masters in parallel.
      Reading these three ports require three states and three properties when what we
      need is one state and one property.

SLIDE 7, EMULATED PORT, INTERNAL:

-1 >>
      We simply move all this into an external module which mimics a SystemC-PPA port interface.
      All interactions with the agents are such that no wait states are called, so that requests are
      forwarded and all agents are unblocked in a single time point just like the RTL.

SLIDE 8, EMULATED PORT, INTERACTION:

-1 >>
       Interaction with the emulated port within the bus matrix now produce only a single state and
       property.
       Fixed-priority arbitration is proven within the bus matrix to be a sound abstraction of the
       arbitration in the RTL.
       It is simple enough to essentially copy-paste into the emulated port.
       This, combined with the uninterrupted execution of the emulated port makes for a sound
       abstraction of the RTL.

SLIDE 9, RTL OVERVIEW:

-1 >>
      To avoid reinventing the wheel, we use an open source AHB architecture.
      This is a trusted VHDL implementation of the interconnect, arbiter and decoder which follow
      the AHB protocol and offer a range of arbitration schemes.

-2 >>
      The architecture is interfaced with agents, which have been designed from scratch.
      They carry out the AHB protocol on one side, and offer a four phase handshake
      on the other. The slave agent extends the data phase by inserting wait states while waiting for a
      handshake from its slave.

      The agents in the generator only support single transfers.
      Burst transactions are implemented outside the generator as a proof of concept.

SLIDE 10, COMPLETENESS:

-1 >>
      Except for the emulated port, property sets prove completeness on the design.
      All I/O signals are listed in the completeness description of both clusters.
      All properties, as well as completeness checks hold, without any constraints.

SLIDE 11, COMPLETENESS CONTINUED:

-1 >>
      When we split a design into clusters, we must ensure that the border
     between the clusters do not present a gap in verification.
     This is achieved by refining the macros connecting the clusters using the same top level
     signal name in both clusters.

-2 >>
     This is mostly a straight forward process, but becomes slightly more tricky with the emulated
     port.
-3 >>
     The request notify in the master agents, and request port in bus matrix are easily refined using
      the top level name for bus request..

-4 >>
     In the other direction, the signals are combined.
     The agent is reacts to ready and grant, and just ready.
     The bus matrix issues ready to all agents, and one grant.
     This is represented in the bus matrix with a logic statement.
     As long as this behavior is guaranteed within the port, it should not leave a gap in verification.

     update_requests_notify models the functionality of grant at the ESL, but it is not sufficient like
     this to satisfy the determination test.
     It is therefore added to the response payload in the shared interface as well, as a purely symbolic
     signal at the ESL.

SLIDE 12, SIMULATION:

-1 >>
      Simulation models are generated for both ESL and RTL.
      They are designed such that they perform operations and verify functionality on equal
      principles.
      Master and slave dummies are designed which perform simple read and write operations.

-2 >>
      The slaves are given ID numbers, which the master agent encodes into the write
      data.

-3 >>
      The slave asserts that this ID matches its own.
      If it is a read transaction, it is the slave who encodes its ID
      in the response data.

-4 >>
      The master compares this ID with its target address.
      If either master or slave detects a mismatch in ID, the simulation is aborted.
      When the total number of transactions reach 1 million, the simulation is ended.

SLIDE 13, RESOURCE COMPARISON
-1 >>
      We can compare the resources required to model the system at both levels.
      The table shows the required I/O pins and state bits needed to model the system.
      The two bottom rows are multiplied based on amount of master and slave agents.

      Identical I/O behavior is modeled at the ESL using a mere fraction of the resources.

SLIDE 14, SIMULATION TIME COMPARISON

-1 >>
      The time required to complete a total of 1 million transfers on the bus has been compared
      between the models.
      The blue, red and beige columns show the time it takes for 1, 2 and 3 masters at the RTL to
      complete the transfers, in seconds. Black is the ESL model.
      The slowest simulations are actually configurations with a single master, and then
      configurations with two masters.
      This is due to latency, or lack of parallelism within the master agents.

      What is shown here is that the ESL model is unaffected by both latency and size. The
      effectiveness depends on the RTL configuration. In any case, the ESL is faster by a factor
      between 11 and 40.
      Larger RTL configurations reside here between three and two masters in required time.
      They are excluded from the figure to keep the graph more readable.
      The ESL as mentioned, remain unchanged for all configurations.

SLIDE 15, PROPERTIES AND PROOF TIMES

-1 >>
      The amount of properties generated from the ESL model is relatively low for any configuration.
      The graph on the left show the property count for the bus matrix dependent on number of slaves.
      One slave requires 21 properties, 15 slaves require 204.
      The amount of properties are independent of amount of masters connected to the system.

      The graph on the right show the proof time of the property sets for a selection of configuration
      sizes.
      It shows that the proof time greatly increases with number of master and slaves.
      Server traffic cause variations in the proof time, but a general trend is shown.
      Proof time increases drastically for large configurations,.
      The longest proof time is 2100 minutes for 15 masters and 15 slaves.
      It was run on an at times busy server using a single core.
      The property set is suitable to run with multiple cores and if busyness is out of the equation,
      proof time is reduced by several factors.

      The master agent is not displayed here because it only has a constant 11 properties and takes
      mere seconds to prove, regardless of configuration size.

SLIDE 16, STARVATION:

-1 >>
      With fixed priority arbitration, the possibility of starvation arises.
      It is a time, or rate dependent phenomenon which need to be explored.
      We bring back simplified versions of the finite state machines from earlier.

      It is easy to see that there is always room for three masters.
      If the pipeline is full, the fourth master and above might starve.

      If the first master returns from the data phase to request, before the second master completes
      its data phase, the fourth master starves.

       Here are actual timings from the RTL.
       In this exact case, the fourth master does not starve.

-2 >>
     The ESL does not show the same timing relation, due to it being an untimed model.
     The same situation results in a fourth master starving.

-3 >>
      In a system of arbitrary complexity, it is hard to predict how starvation will occur
      at the ESL in relation to the RTL.

      If Y is smaller, and K is bigger, more masters starve
      if K is smaller and Y is bigger, less masters starve.

      What matters the most is the proportion of K to Y at the ESL compared to the RTL.
      If more masters starve in the ESL model compared to the RTL model, we say the ESL
      model over approximates starvation and all simulations are safe.

      The values of K and Y will vary depending on what level of abstraction a designer implements
      in the masters and slaves.
      The value of K may be 1 at the ESL, but abstraction in a slave may or may not provide
      a value of for example 6 at the RTL.
      If starvation is over or under approximated is now dependent on the level of abstraction
      within the masters.

SLIDE 17, STARVATION COMPARISON
-1 >>
      We compare starvation across the two models.
      The graph on the left is the RTL, the right is the ESL.
      The master dummies insert delays between each transfer.
      For the RTL you see on the Y axis that the master dummies delay for Y clock cycles before
      initiating a new transfer.
      For the ESL the master dummies call a wait statements of y picoseconds before initiating
      a new transfer.
      The X-axes show masters receiving a grant, note that priority decreases upwards.
      The slope of the curves increase with values of K.

       When the transfers are out of range, the timing relations are as shown in the recent figure.

       Here the RTL shows four masters granted with zero added delay, whereas the ESL shows only
       three.
       Starvation in this case is over approximated.

-2 >>
      What the results show here, is that the RTL has varying and increasing values for K
      depending on transfer type and status.
      None of these factors are shown at the ESL.
      This causes some concern that starvation is not always over approximated.
      When bursts are implemented, this may be further aggravated if you consider
      the K value of a 16 beat burst transaction at the ESL vs RTL.

     We have currently no guarantee that for example 6 wait statements, or wait time always equates
      a minimum of say 23 clock cycles.
      This should be ensured somehow.

      It may be possible to implement a safety net, in the form of a monitor.
      This monitor can keep track of the transfer types, and perhaps even include some
      information on abstraction.
      In any case, if safety limits are violated the simulation is aborted and the user is notified.

-3 >>
       Here the slaves insert a random delay between 1 and Y, and the PPA port interfaces
       wait between 1 and Z.
       The slopes increase exclusively in the right direction, so random times are safe to use and
       monitor as well.
       This is provided that the PPA ports dont include zero time in the randomness, if masters
       wait nonzero, and bus waits zero, even just once, all masters are granted.

SLIDE 18, CONCEPT: BURST TRANSFERS:

-1 >>
      Burst transactions have been implemented as a proof of concept.
      There are far too many details to cover them all, so only a general implementation is described
      now.

      The payloads of most existing ports are extended to account for burst transactions.
      They are here shown in purple.
      These payloads can be shared between all transfer types. The payloads can not be extended
      on the shared out ports, which accounts for the majority of the interface between master agent
      and bus.
      Shared out ports are not practical to model burst transactions.

-2 >>
      For this reason extra ports are added to model the burst transfers on the
      master side of the interface.
      Update requests is extended to handle burst reads in the matrix.
      A helper payload over the request port is used so the emulated port can distinguish between the
      transfer types.
      This payload is also used to transfer the burst write data at an earlier stage, so that it
      can reach its target in simulation before the data phase is over.

SLIDE 19, BURSTS CONTINUED:

-1 >>
      The payloads can include address, data and any control signal in need of determination.
      Control signals are smaller and are concatenated as in line 2.
      They are shifted left before they are or’ed in real code.

      All variables relevant to the burst in question are assigned their values.
      All irrelevant variables, in this case address and data above 3, are assigned zero.
      Affected shared ports are simply assigned the values of the final beat.

-2 >>
      The macros are refined such that the signal is time shifted, or eliminated
      based on how many beats of the burst there are, hwdata4 is shifted back 11 cycles for a 16 beat
      burst, 3 cycles for an 8 beat burst, and eliminated for 4 beat bursts.

      For burst reads, many signals need a condition for trailing error responses as well, adding one
      condition with an additional cycle to each burst type and length.

SLIDE 20, BURSTS CONTINUED 2:

-1 >>
      The proof of concept does not prove completeness on the design. But it is feasible to do so.
      The main challenge is determining the outputs to both clusters, specifically on the
      interface between the master agents and the bus.

      Certain control signals as well as address and data must be determined for each beat of the burst.
      Certain beats span across multiple cycles, where address and data are unchanged and should be
      allowed undetermined to avoid duplicate variables.

-2 >>
      The duration of each burst must always be known.
      This means that undefined incremental burst transfers must be excluded from the
      implementation.

      Luckily, any wait states inserted by the slave agents, which play a part in the duration
      of a burst property is known beforehand, so no constraints are needed there.

SLIDE 21, OUTLOOK:

-1 >>
      There is still work that is needed on this project, which require further
       research

-2 >>
      A formally verified alternative to the emulated port is needed. This might be a dedicated port
      interface which is added to SystemC-PPA.
      It might also be a simpler workaround which allows multiple ports to receive the same event
      notify.
      Without such an alternative, it is not safe to modify the interface, or implement any other
      arbitration scheme.

-3 >>
      For fixed priority arbitration, we need more research into the exact timings which ensure
      safe simulation at the ESL, such that a monitor can be implemented.

SLIDE 22, CONCLUSION:

-1 >>
      What is completed in this project is that AHB systems can be generated which carry out
      single transfers.
     The properties are successfully refined automatically to hold on the design, for any configuration

-2 >>
      The system is modeled with a high level of abstraction at the ESL
      Simulations are orders of magnitude faster than the RTL.

-3 >>
      The proof of concept show that burst transfers are feasible on this system.
      But as mentioned, we need more research into the emulated port interface and especially
      the monitor.